## Slide 1: FIP AOI inspection level verification with BR213 parts

## Slide 2
Information Security
This presentation contains Corning Restricted information and is intended solely for those with a need to know. It may not be distributed, in whole or part, in any form by any means, or by any person or organization without authorization from Corning Incorporated.

## Slide 3: FIP AOI inspection level verification with BR213 parts
FIP AOI inspection level verification with BR213 parts |  |  | 
Purpose | The purpose of this EEP is to verify AOI level by comparing AOI and master inspection data(such as Defect size range ,Defect size range , Defect count, Defect type, Defect location, Yield loss gap) with BR213 parts. |  | 
Parts needed | 5 kinds of parts, 1000 pcs per part. Each part collects 3 rounds, 1st round uses 500 pcs inventory NG parts, 2nd and 3rd round use 250 pcs MP NG parts (Different AR round). |  | 
Process | Process Description | Owner | Time
Collecting Part | Collect Inventory NG part(500)，MP NG part(500) | Yin, Winnie | 7/2-8/31
Washing part C5 | Wash the wiping stains due to inventory and handling | Zhang, Peko | 7/23-8/31
AOI | AOI | Zhang, Peko | 7/23-8/31
Laminating | Laminating | Zhang, Peko | 7/23-8/31
Master mapping | Do full inspection of all defects, record the defects dimension (Length, Width, Diameter, Distance etc.) and mapping all defects locations on the drawing. | Yin, Winnie | 7/23-8/31
Review AOI data | Review the AOI database data(defect location defect dimension) | Yin, Winnie Zhang, Peko | 8/1-8/31
Summarizing data | VLOOKUP(AOI data, Master data, Exact Match) VLOOKUP(Master data, AOI data ,Exact Match) | Yin, Winnie Zhang, Peko | 8/1-8/31

## Slide 4
Fix a filter area and calculate the average gray values A1
Fix a +/-deviation pulse with A1 to identify the threshold A2
Locate the outliers pixels by threshold A2
Fix a cluster distance A3
To cluster the defect
Gerent the Min the rectangle and calcite the pixels area and rectangle area
Gradient threshold:
Filter area:
Deviation:
Cluster distance:
The difference between defect gray values and others values: to classification defect
The area of minim rectangle
The ration of minim rectangle are and defect pixels area
How to calculate the diff?
What the algorithm of gerent minim rectangle?
Plane detection
Defect Detection Process

## Slide 5
Loading Part
Washing part
C5
AOI
Laminating
unloading
Double Check
Generate Pieces name
Printing pieces name
Master mapping
Unloading Car
Review AOI data
Summarizing data
Match the master mapping defect with AOI data
For example:
Master record: Dot(0.15<D<0.2,A1-BM1)
AOI data:
Double check
Logical?
检测到NG就停吗？
The match level of Location and size
Master Mapping steps
检测到NG就停吗？
Master 先检 再AOI 不然AOI检查之后会有额外的划伤，那么mater就不能标记
如果master先检，要在parts上做标记吗 标记之后要擦掉吗 不擦掉的画会影响成像吗
手工标记
复判标记
怎么保证人检验的准确性（还是相信就可)
4个master是平行的吗
4个master的姓名有确定吗
检查到NG就停吗
检查时间
AOI是检查到NG品就停吗
YP的Tool 会记录缺陷的位置（x,y)坐标，缺陷类别，缺陷的尺寸（点缺陷的D)?